## Slide 1: Design for testing and FA
Yariv Shlivinski

## Slide 2: Design and Layout for failure
“Success is the ability to go from failure to failure without losing your enthusiasm.”

## Slide 3: Design and Layout for testing, failure analysis and failure mitigation
Two kinds of tests:
  R&D
  Production line
Two kinds of FA:
  R&D+Q&R
  Field remote

## Slide 4: Design and Layout for Lab testing

## Slide 5: Test points
Lab
  For easy testing make sure to have TPs on the top side.
  GND TP close to the tested module.
  Try to make the TPs as accessible as possible.
  Do not sacrifice performance for testability!
    Stubs
    Noise collection.
D1999BB - PortiaX

## Slide 6: Test points
ATE
  For injecting power and Electronic load connection use four ATPs for Kelvin connection.
  In case of high current make room for large ATP
  Default ATP is 60mil for 0.75mm pin at the fixture. Can be used for currents lower than 1.5Amp.
  If constraint may use 40mil pad it is not recommended.
D1999BB - PortiaX

## Slide 7: Auxiliary
Secondary auxiliary
  Internal Low DC -> Low DC
  Only black box testing
  Need to be able to separate input and output for testing.
D1999BB - PortiaX

## Slide 8: Auxilaiary
Main auxiliary:
  In most cases the output is a diode. It is easy to inject voltage at the output to test secondary power supplies.
  White box
  Need to measure internal parameters:
    Loop transfer function
    Gate signals
    Switch voltage
    Switch current?
    Input/output voltage/current.

## Slide 9: Main Auxilaiary
Jupiter 3

## Slide 10: Bode 100
The following figure shows the feedback loop of the circuit and indicates the suitable injection point. The impedance looking backwards equals the output impedance of the converter which is very low (in the range of several mΩ). The impedance looking in direction of the loop is formed by the compensator and the voltage divider and is in the range of several kΩ.

## Slide 11: Main Auxiliary
Add small serial resistance in feedback path.
  Network analyzer (Bode 100) connection point
C425
68p
*
R432
10K
R433
10K
*
R443
3K
U402
FOD817A3SD
1
2
4
3
AC_FB
D410
BAT54XV2
*
2
1
AC_VREF
2.5V_AC
R437
210
R440
1000
C436
1000n
*
C428
1u
12V_AC_FB
R428
10
R431
1K
2.5V_AC
2.5V_AC
R442
4.99K
ZD400
LM431BIM
3
1
2
C438
47n
R434
49.9K
R427
470
DGND

## Slide 12: Auxiliary Current FB
Do not add test points to CS.
  Current sense is very sensitive to noises. Avoid having stubs/antennas on that line.
Fsw=100kHz
R426
20K
CS_AC
TP407
C432
150p
R415
13
ACDC_CTRL-
AC_FB
AC_Rt/Ct
Q402
MSJU04N80A
4
1
3
U401
UCC28C54
1
COMP
5
GND
3
CS
4
RT/CT
7
VDD
2
FB
6
OUT
8
VREF
AC_VREF
R421
4.99K
R419
30
C413
2.2n
R440
1000
D409
BAV21
*
2
1
AC_PWM
R425
20K
AC_VREF
ACDC_CTRL-
CS_AC
Q401
2N7002KW
1
2
3
C439
100n
C406
100p
*
R412
20
*
R422
1.3
AC_Rt/Ct
50% DUTY
R416
20
*
AC_PWM
ACDC_VCC
D403
1N4148
2
1
R438
30K
R423
1.3
AC_COMP
R429
1000
AC_FB
R420
10K
Q405
MMBTA56
3
2
1
C438
47n
C405
100n
AC_COMP
R418
1K
AC_VREF
ACDC_CTRL-

## Slide 13: Debug card Connection V4
Debug Card is connected and used only in lab.
  When not used SPI lines become stubs and antennas. Signal is both distorted and collects noises.
FPGA
MNGR
PWR
DBG
SPI
SPI
SPI

## Slide 14: Example V4
MNGR to Debug connector 20cm
FPGA to Debug 25cm
Solutions:
  Place Debug connector close to manager
  Use 0 ohm resistors to disconnect.
FPGA
MNGR
PWR
DBG
SPI
SPI
SPI

## Slide 15: Example V4 (what we intended 🙂)
15
FPGA
MNGR
PWR
DBG
SPI
SPI
SPI
RES

## Slide 16: Example V4 (What we implemented ☹ )
Even best solutions should be implemented correctly.
MNGR
RES

## Slide 17: JTAG
JTAG resets the DSP
To avoid false RESET the line should be pulled as close as possible to the DSP pin.

## Slide 18: Design for Failure analysis and prevention
“There are known knowns, things we know that we know;
and there are known unknowns, things that we know we don't know.
But there are also unknown unknowns, things we do not know we don't know.”
Donald Rumsfeld

## Slide 19: Design for Failure analysis and prevention
Failure cannot be predicted
  What to measure?
  How much money/effort/space should we invest?

## Slide 20: Temperature
Temperature is a good predictor and sign for system/device failure
Temperature sensing is easy to implement.
Sense lines tend to be long from power train to DSP.
  Noise peak-up and injection.
  Power planes cut through.
Clearance/creepage: Temperature sense lines are low voltage signals that are routed in high voltage areas.
  Solution: Use different layers for temp sense and power.
  Downside: Wasting power layers for telemetry.
Need to find the correct balance between telemetries and performance.

## Slide 21: Temperature sensing
Place as much sensors as possible.
Temperature changes are slow, and signal is not sensitive.
Possible to use mux.
Standard telemetry does not support so many measurements but in case of need software may be changed and events added.

## Slide 22: Temperature sensors V4

## Slide 23: Temperature sensors V4

## Slide 24: System Temperature measurement
System level testing
  What is the root cause?
Performance depends on ambient
  Need calibration temperature sensor
  Heat-sink measurement?
Sensor should be located as close as possible to device in question
  Which devices are most important?
  Clearance creepage.

## Slide 25: RSS2.5
Analog isolation
The driver has analog isolated port which translates high voltage domain signal to low voltage domain PWM

## Slide 26: RSS2.5
Analog isolation

## Slide 27: V4
Clearance and creepage require larger distance. How good is the thermal coupling.

## Slide 28: Connector Temperature
Connectors are weak points.
  Power connector detachment can cause fire
  Connection deterioration is usually gradual
Solution:
  Measure temperature near the connection point.
  In case of deterioration impedance and temperature rise.
  How can we couple the sensor to the point of interest?

## Slide 29: CTM (H1300)
Maximum metal around thermistor
For optimizers clearance creepage requirements are low.